## Slide 1: Risk Assessment for Benzene

## Slide 2: What is Risk?
Cause
Effect
What’s the probability that something happens?
Risk

## Slide 3: Risk is Inherent to Everyday Life

## Slide 4: Quantitative Risk Assessment for Human Health
The characterization of the potential adverse health effects of human exposures to environmental hazards (NRC 1983)
https://www.nationalacademies.org/publications/366
https://www.nationalacademies.org/projects/BEST-K-05-02-A/publication/12209

## Slide 5: Quantitative Risk Assessment for Human Health
Hazard Identification
Exposure Assessment
Dose-Response
Risk Characterization
What’s at issue?
How much increases risk?
How much is around?
What is the probability of disease?

## Slide 6: Hazard Identification
Hazard Risk
What’s at issue?
Review Data
What health effects are associated with the hazard?
Describe Mode of Action
How does the hazard interact with the body?
Evaluate Evidence
How strong is the evidence?
Review Exposure
How does one encounter the hazard?

## Slide 7: Hazard Identification
Review Data
What health effects are associated with the hazard?
Describe Mode of Action
How does the hazard interact with the body?
Evaluate Evidence
How strong is the evidence?
Review Exposure
How does one encounter the hazard?
Non-Cancer: Decreased White Blood Cells (EPA)
Occupationally
Numerous studies have found that sufficient dose can lead to reduced white blood cell count and an increased risk of AML
Cancer: Leukemia (specifically Acute Myeloid Leukemia (AML)) (EPA)
Inhalation
Environmentally
https://en.wikipedia.org/wiki/Benzene#/media/File:Benzene-aromatic-3D-balls.png
https://en.wikipedia.org/wiki/Benzene#/media/File:Benzene_sample.jpg

## Slide 8: Exposure Assessment
Important Details for Assessing Exposure
Type
Chemical composition
Intensity
Intensity (i.e., concentration)
Frequency
How frequently this exposure occurs
Duration
How long it occurs
Route
How far from the emission point to the receptor
How much is around?

## Slide 9: Exposure Assessment
Exposures vary over time
Exposures can be summarized as:
Minimum
Median (50th Percentile)
Arithmetic Mean
Geometric Mean
Maximum
For a risk assessment we are generally concerned with the arithmetic or geometric mean of exposures with an appropriate averaging time

## Slide 10: Units of Measurement
Micrograms per cubic meter (µg/m3)
  1 µg = 0.000001 g
  A single grain of table salt is 60 µg
  On average, an adult breaths 16 m3 of air per day
  1 m3 = 264 gallons
1 µg/m3 = 1/60 of a grain of salt mixed in 264-gallon containers

## Slide 11: Units of Measurement
Parts per billion (ppb)
  Amount of something in something else
  1 ppb = 1 second in 32 years
    (1 year = 31,540,00 second)
Can convert from µg/m3 to ppb
Parts per million (ppm)
  1 ppm = 1000 ppb
  1 ppm = 1 second in 11.5 days
Benzene:
1 ppb = 3.19 µg/m3 x 24.45 ÷ 78.11 g/mol
https://www.chemaqua.com/en-us/blog/2019/10/29/what-is-ppm/

## Slide 12: Exposure Assessment – Fenceline Monitoring (Unadjusted)
EPA’s Reference Concentration
99.9% of measurements are below this line
Arithmetic Mean (1.6 µg/m3)
The fenceline concentrations will be higher than concentrations in the nearby community

## Slide 13: Fenceline Data is Not Representative of Personal Exposure
Fenceline data allows some insights into emissions.
However, because of the distance between these monitors and where people are located, modeling must be used to estimate concentrations of benzene in areas of interest.
Modeling allows for consideration of meteorological effects (primarily wind direction and wind speed).
Where we have data
Where we want estimates
Notes: Change legend to “Modeled […]

## Slide 14: Exposure Assessment – AERMOD Results
Rank | Annual Concentrations |  |  | 
 | Benzene (µg/m3) | UTM East (m) | UTM North (m) | Year
1 | 0.1849 | 412739.75 | 4610192.33 | 2024
2 | 0.1746 | 412739.75 | 4610192.33 | 2023
3 | 0.1744 | 412739.75 | 4610192.33 | 2021
4 | 0.1720 | 412739.75 | 4610192.33 | 2018
5 | 0.1667 | 414174.75 | 4612948.17 | 2020
6 | 0.1660 | 414174.75 | 4612948.17 | 2023
7 | 0.1648 | 412739.75 | 4610192.33 | 2020
8 | 0.1610 | 414174.75 | 4612948.17 | 2021
9 | 0.1584 | 414174.75 | 4612948.17 | 2024
10 | 0.1562 | 414174.75 | 4612948.17 | 2019

## Slide 15: Exposure Assessment – Comparisons
Sources: US Environmental Protection Agency, World Health Organization, Valisure, Int. J. Environ. Res. Public Health 2021, DOI: 10.3390/ijerph18041872. Reproduced from Bettenhausen (2021):
14.3 -20,478.2 µg/m3
143.3 µg/m3
6.7 µg/m3
12.8 µg/m3
7.2 µg/m3
Outdoor Air, Rural: 1.6 µg/m3
Outdoor Air, Suburban and Cities: 7.7 – 10.2 µg/m3
15.4 -194.5 µg/m3
Notes: Add AL, scale text

## Slide 16: Sources of Benzene
“The most significant general population exposures [to benzene] are in indoor air from sources such as evaporative emissions from cars in attached garages, or from cooking on gas stoves, from smoking, and from automobile related activities such as pumping gasoline.” (CDC ATSDR 2024)

## Slide 17: Dose-Response (Non-Cancer)
Reference Concentration (RfC):
“The continuous inhalation exposure that is likely to be without an appreciable risk of health effects during a lifetime” (EPA)
How much increases risk?
Equivalent to 30 µg/m3

## Slide 18: Dose-Response (Cancer)
Inhalation Unit Risk (IUR):
“The increase in lifetime cancer risk from a lifetime (70 years) of exposure” (EPA)

## Slide 19: Dose-Response
Endpoint | Exposure Route | Dose-Response Metric | Acceptability Criteria
Non-Cancer: Reduced White Blood Cell Count | Inhalation | Reference Concentration (RfC): 30 µg/m3 | MOS >1
Cancer: Leukemia | Inhalation | Inhalation Unit Risk (IUR) (per µg/m3): LB: 2.2 x 10-6 UB: 7.8 x 10-6 | Lifetime Cancer Risk between: 1x10-4 (1 in 10,000) 1x10-6 (1 in 1,000,000)
Source: EPA IRIS
https://www.epa.gov/fera/risk-assessment-other-effects
https://www.epa.gov/iris/basic-information-about-integrated-risk-information-system

## Slide 20: Risk in Perspective
Lifetime ‘Risk’ | Event
1 in 95 | Dying in a car crash
1 in 2,461 | Dying from choking on food
1 in 10,000 | EPA Upper-End Acceptable Risk
1 in 39,192 | Dying in a severe storm
1 in 44,499 | Dying from a dog bite
1 in 340,733 | Dying from fireworks
1 in 1,000,000 | EPA Lower-End Acceptable Risk
1 in 1,048,576 | Flipping a coin 20 times and getting all heads
https://injuryfacts.nsc.org/all-injuries/preventable-death-overview/odds-of-dying/
https://www.floridamuseum.ufl.edu/shark-attacks/odds/compare-risk/death/

## Slide 21: Risk Characterization (Non-Cancer)
Max Annual Offsite Concentration (µg/m3) | EPA Reference Concentration (RfC): | MOS | Conclusion
0.18 | 30 µg/m3 | 30/0.18 = 167 | Acceptable
Reference Concentration (RfC):
The continuous inhalation exposure that is likely to be without an appreciable risk of health effects during a lifetime (EPA)
What is the probability of disease?

## Slide 22: Risk Characterization (Cancer)
Max Annual Offsite Concentration (µg/m3) | EPA Reference Inhalation Unit Risk (per µg/m3): | Lifetime Cancer Risk (70 years) | Conclusion
0.18 | LB: 2.2 x 10-6 UB: 7.8 x 10-6 | LB: 4 x 10-7 (4 in 10,000,000) UB: 1 x 10-6 (1 in 1,000,000) | LB: Acceptable UB: Acceptable
Inhalation Unit Risk (IUR):
The excess lifetime cancer risk from a lifetime of exposure (EPA)
EPA aims for a lifetime cancer risk between:
1x10-4 (1 in 10,000) to 1x10-6 (1 in 1,000,000)

## Slide 23: Conclusions
Risk is inherent to everyday life
Quantitative risk assessment is a formalized method for estimating risk
  Hazard Identification
  Exposure Assessment
  Dose-Response Analysis
  Risk Characterization
The average fenceline concentration was 1.6 µg/m3
The maximum annual offsite concentration was 0.18 µg/m3
These values are consistent with ambient and indoor concentrations of benzene
The risks of adverse health effects in the community were considered de minimis and within the range considered acceptable by EPA.